## Slide 1: SolidWorks Seminar series: Introduction to SolidWorks
FRC 2468 Appreciate
Lewis Jones

## Slide 2: Overview
Week 1:
  SolidWorks Introduction
  SolidWorks Assembly: Mates
Week 2:
  Assembly Project: Robot Assembly Using Parts Library
Week 3:
  SolidWorks Parts: Sketching Tools, Boss Extrude, Extruded Cut
  SolidWorks Parts: Revolve Extrude, Linear, Rotary, and Mirror Patterns

## Slide 3: Overview
Week 4:
  Parts Project: 3D Printable Accessory
  Parts Project: Gearbox Plate
Week 5 and 6:
  Final Project: Robot Complete CAD
  Review
  SolidWorks: Project CAD Management

## Slide 4: What is CAD and SolidWorks?
CAD
Stands for Computer Aided Design
Used in almost any kind of engineering
Very important in being successful with the final product
SolidWorks
  CAD Tool
  2 types of files: Part and Assembly

## Slide 5: SolidWorks File: Part
Part
  Individual component
  Can be assigned different properties (color, density, material)

## Slide 6: SolidWorks Assembly
Assembly
  Made up of Parts
  Can be rigged to move just like the real mechanism

## Slide 7: CAD File Types
SolidWorks
  [Part].SLDPRT
  [Assembly].SLDASM
Non-SolidWorks Software
  [CAD].STEP

## Slide 8: SolidWorks Navigation
Open SolidWorks file named
Swerve-Module.sldasm
Navigate between files by using the buttons on the tool bar

## Slide 9: Navigating a Model
Zoom in and out by using the mouse wheel
Pan the camera around the object by pressing down on the mouse wheel and moving the mouse
View orientation button in the top of the viewing area brings up options to view the part head-on from a plane

## Slide 10: View Orientation

## Slide 11: Assembly

## Slide 12: Assembly Navigation
The parts and sub-assemblies in the assembly are shown on the left in the Design Tree section
If you click on a part in the assembly, the name of the part will be highlighted in the Design Tree section
Individual parts and sub-assemblies can be opened by right-clicking on the part names or the parts in the assembly and clicking “Open Assembly” or “Open Part”
If the Design Tree section is beginning to get overcrowded, you can right click in the section and select “Collapse Items”

## Slide 13: Useful Evaluate Tools
Notes: 15:00 minutes

## Slide 14: Measure
Measure Tool can find the distances between planes, edges, points, centers of circles, etc.

## Slide 15: Mass Properties
Mass Properties Tool can find the density, mass, and center of mass of assemblies or selected parts

## Slide 16: Units
The units that SolidWorks defaults to can be changed by clicking on the button in the bottom right corner

## Slide 17: Transparency
Parts in an assembly can be put in a “transparent mode” to allow the user to see other parts that were hidden under it

## Slide 18: Section View

## Slide 19: Section View
Section View allows the model to be viewed as if it was “cut” along a plane
Select the plane to cut by changing the reference plane and the distance/angle to that plane

## Slide 20: Mates
The basic function in assemblies
Creates a relation between parts such as:
  Coincident
  Concentric
  Tangent
  Parallel
  Perpendicular
  Distance
  Angle

## Slide 21: Mate Menu

## Slide 22: Mate Menu

## Slide 23: Coincident Mate
Use this mate to put different parts together along a plane or an edge

## Slide 24: Coincident Mate

## Slide 25: Concentric Mate
Mates two circles so that they are concentric (share the same center)

## Slide 26: Concentric Mate

## Slide 27: Wheel Assembly
You will now put together a wheel assembly, made up of a wheel, hubs, screws, and nuts
Navigate to CAD Files > Wheel Assembly
You are given instructions in the form of a picture as well as all the parts necessary to put together the wheel assembly in the folder
Put it together!

## Slide 28: Tangent Mate
Makes a plane tangent to a cylinder/circle

## Slide 29: Tangent Mate

## Slide 30: Other Standard Mates
Parallel
  Makes two planes or edges parallel to each other
Perpendicular
  Makes two planes or edges perpendicular to each other
Distance
  Sets a static distance between two planes
Angle
  Sets a static angle between two planes

## Slide 31: Multiple Mate Option
Useful when mating multiple objects to a single plane
Imagine “putting objects on top of a desk”

## Slide 32: Mating Planes
Planes of the parts and the assembly can be selected by opening the mini-Design Tree when the Mate Menu is open

## Slide 33: Advanced Mate

## Slide 34: Symmetric Mate
A symmetry plane and two other planes are selected
The other two planes become symmetric across the symmetry plane

## Slide 35: Symmetric Mate
Very useful for assemblies that may change size in the future

## Slide 36: Limit Distance Mate
Sets up limits for the distances that two planes can be at

## Slide 37: Distance Limit Mate

## Slide 38: Mechanical Mate
Mates that display functions that are difficult/impossible to show through the Standard and Advanced mates but are often used in mechanical engineering

## Slide 39: Slot Mate
Similar to the limit distance mate, this mate limits an object so that it can only move within the bounds of a slot

## Slide 40: Screw Mate
Set up by selecting a cylinder (a threaded hole in real life) and a rod (a screw/bolt in real life)
Distance per rotation of the screw is inputted and the CAD model prevents movement of the screw model unless it is spun

## Slide 41: Gear Mate
The diameter of each gear is inputted and the model rigs the gears to spin in sync when one of them spins

## Slide 42: Parts

## Slide 43: Part Navigation
Open SolidWorks and Click “New” in the top left section of the window
Click “Part” on the window that pops up then “OK”

## Slide 44: Creating Sketch
Click on “Sketch” in the new tool bar at the top and it should tell you to select a plane
Select the “Top Plane” for now by clicking on the top plane in the 3 dimensional view. You can also select by clicking on “Top Plane” in the design tree

## Slide 45: Sketching Tools
On the top is the tool bar with all the different ways to sketch shapes on the plane you have selected
The small downwards pointing triangle next to each item suggests there are different ways of drawing the shape (e.g. Drawing a rectangle)
Different ways to draw can help you immensely in giving the new feature the relation you want with the other entities in the sketch

## Slide 46: Smart Dimension
Smart Dimension allows the user to set specific dimensions to entities in sketches such as distance, length, diameter, etc.
It’s called smart dimension because YOU need to be smart to use it correctly. If you have the “correct” ones set, changing dimensions in the future would be very easy

## Slide 47: Relations
OH MY GOD USE THESE PLEASE!!!
You can set different relationships using this tool and it simplifies a lot of sketches SIGNIFICANTLY
Example on next page…

## Slide 48: When you don’t use Relations

## Slide 49: When you do Use Relations

## Slide 50: Relations
Click on an entity
Press down CTRL and click on another entity
Select which relation you want

## Slide 51: Construction Geometry
When you draw an entity, you don’t always want it in the final product and just need it as a reference.
To change the entity to a “construction geometry”, select the entity and click on the “For Construction” option on the left side

## Slide 52: Fillets
Pronounced “fill-et”…
NOT “fill-eh-y”
Smoothes a sharp corner in sketches (you can do it with a 3 dimensional parts too if you want)
Select a point or two lines to fillet the corner

## Slide 53: Mirror Entities
Tool that allows selected entities to be mirrored across a line/axis

## Slide 54: Let’s Try Sketching
Open a new part and put together a sketch that follows the dimensions given in the picture called “Gearbox Plate” on the Front Plane

## Slide 55: Extruded Boss/Base
Makes a sketch “pop out” and become 3 dimensional
Once your sketch is done, go to the “Features” in the tool bar tabs at top and then click on “Extruded Boss/Base”

## Slide 56: Extruded Boss/Base
In the options, you can set the thickness of the part and the direction the material is extruded
You can also select certain sections to be or not to be extruded using the “Selected Contours” option

## Slide 57: Extruded Cut
Opposite of Extruded Boss/Base
Cut out material from existing part based on a sketch
Options are very similar to Extruded Boss/Base, try to use “Through All” if possible instead of raw dimensions

## Slide 58: Configurations
Allows there to be multiple versions of the same part
Dimensions can be shared between different versions
Especially useful for gearbox plates

## Slide 59: Adding a Configuration
Click on the third tab of the “Design Tree” section on the left side

## Slide 60: Adding a Configuration
Right click on the parent configuration and click “Add Configuration”

## Slide 61: Configurations Tip
In a new configuration, you can add new features or suppress features but all configurations must share the same features

## Slide 62: Let’s Try configurations
Make a new configuration called “Frame Attachment” for the gearbox plate
Make cuts to match the dimensions of the reference picture “Frame Attachment”

## Slide 63: Complete Gearbox

## Slide 64: Offset Entities
Creates a parallel line that is offset by a set distance from a previously existing entity

## Slide 65: Convert Entity
Converts the outline of features into the sketch that is currently open

## Slide 66: Plane
To create a new plane to sketch on, click on the “Reference Geometry” from the features menu and then “Plane”

## Slide 67: Plane
You can now select existing entities and planes to set the location of the new plane

## Slide 68: Plane

## Slide 69: Axis
Creates an axis that can be referenced by features and sketches

## Slide 70: Axis

## Slide 71: Linear Pattern
Can be done inside the sketch or as a new feature (feature is usually better since configurations can change the number of holes, etc.)

## Slide 72: Fillet Feature
Again, Fill-ETS
You should be using this instead of the sketch fillet in most cases

## Slide 73: Revolved Boss/Base
How would you create a sphere using extruded boss/base?
It’s impossible
Revolved Boss/Base is used when you want to create something like a sphere or a door knob where the entity is symmetric around an axis

## Slide 74: Revolved Cut
Opposite of revolved boss/base
Cuts away material in a circular direction

## Slide 75: Revolved Cut

## Slide 76: Hole Wizard
SolidWorks puts in a hole with the correct dimensions for the screw/bolt you want to put in the hole

## Slide 77: Hole Wizard

## Slide 78: Hole Wizard

## Slide 79: Hole Wizard

## Slide 80: Strategic Design

## Slide 81: overview

## Slide 82: Strategy
Read the rules, reread the rules, understand the rules
Come up with the best strategy
  What action(s) generate the highest score for the least amount of time/work?
  Chokehold strategy: A strategy that, if set up correctly, guarantees victory
  Remember that defense can be just as effective as offense
  Being able to do one action very well, instead of being mediocre at many actions, is almost always better
  Always know your limitations! “Elegant” and “Simple” designs are almost always the best!

## Slide 83: Actions
Come up with a list of actions that the robot might do for the strategy and mark them as:
  Demand
  Preferred
  Wish
Example:
  Robot is able to move: Demand
  Robot is able to hold a game piece: Demand
  Robot is able to hold 3 game pieces: Preferred
  Robot is able to hold 5 game pieces and pick them all up in 10 seconds: Wish
Be quantitative about the actions
  How long will it take?
  How many game pieces?
  How far does the robot travel?

## Slide 84: Ring It Up!
Strategies?
Actions?

## Slide 85: Drive Train
The most important component of your robot
The most important qualities of drive trains are:
  Reliability
  Axis's of motion
  Resource intensiveness
  Simplicity/complexity
Wheel Type
  Traction/pneumatic
  Omni
  Mecanum

## Slide 86: Tank Drive
Tank drive
  West Coast Drive
  Prometheus-style Drive
  Four Wheel Drive
Pros
  Simple
  Effective
  Reliable
  Pushing Power (Based on number of motors)
Cons
  Can’t drive side-ways

## Slide 87: Slide/H-Drive
Slide/H-Drive
  Made up of omni-wheels facing perpendicular directions
Pros
  Fairly Simple
  Able to strafe (move sideways)
  Fairly Reliable
Cons
  No pushing power
  Can’t traverse rough terrain/ramps

## Slide 88: Mecanum Drive
Mecanum Drive
  Made up of (usually) four mecanum wheels
Pros
  Simple hardware
  Able to strafe
Cons
  Difficult programming
  Little pushing power
  Can’t traverse rough terrain
  or ramps
  Expensive Wheels

## Slide 89: Holonomic Drive
Holonomic Drive
  Four omni wheels set up in the corners of the robot with the axles pointing at the corners
Pros
  Fairly simple hardware
  Able to strafe
Cons
  Difficult programming
  Little pushing power
  Can’t traverse rough terrain
  or ramps
  Mounting the wheels to be 45 degrees to the frame can be a pain

## Slide 90: Swerve Drive
Swerve Drive
  Made up of swerve modules where each module can spin the wheels as well as change the direction that the wheels are pointing
Pros
  Pushing Power
  Able to strafe
  Can traverse rough terrain/ramps
Cons
  Really complex
  Weighs a ton
  Can be unreliable
  Difficult Programming
  EXPENSIVE

## Slide 91: Picking a Drive Train
Make a weighted objectives table
  5 is great, 1 is bad
  Weights are dependent on:
    The game
    Your strategy
    Resources

## Slide 92: Picking a Drive Train